MASTER CODE FOR ROVER COMMUNICATION

CODE:

#include <esp_now.h>
#include <WiFi.h>
#include <esp_wifi.h>
#include <CytronMotorDriver.h>

// ================= MOTOR DRIVER =================
CytronMD motor1(PWM_DIR, 23, 18);
CytronMD motor2(PWM_DIR, 5, 21);

#define CHANNEL 1

// ================= COMMAND STRUCT (MASTER → SLAVE) =================
typedef struct struct_message {
  float fieldLength;
  float fieldWidth;
  float rowSpacing;
  bool startAuto; // true = start serpentine, false = STOP
} struct_message;

struct_message incomingData;

// ================= TELEMETRY STRUCT (SLAVE → MASTER) =================
typedef struct telemetry_message {
  float moisture;
  float temperature;
  float ec;
  float ph;
} telemetry_message;

telemetry_message telemetryData;

// ================= FLAGS =================
bool startSerpentineFlag = false;
bool stopNow = false; // STOP FLAG

// ================= MOVEMENT SETTINGS =================
float forwardSpeedMps = 0.30;
float shiftSpeedMps = 0.25;
int turnTime90 = 5000; // ⭐ 5 SECOND TURNS ⭐

// ================= MASTER MAC =================
uint8_t masterMAC[] = { 0xD4, 0xE9, 0xF4, 0xED, 0x21, 0x38 };

// ==========================================================
// SEND TELEMETRY
// ==========================================================
void sendTelemetry() {
  esp_now_send(masterMAC, (uint8_t*)&telemetryData, sizeof(telemetryData));
}

// ==========================================================
// RECEIVE COMMAND FROM MASTER
// ==========================================================
void OnDataRecv(const uint8_t *mac, const uint8_t *data, int len) {

  if (len != sizeof(struct_message)) return;

  memcpy(&incomingData, data, sizeof(incomingData));

  if (incomingData.startAuto) {
    Serial.println("📥 START Command Received");
    stopNow = false;
    startSerpentineFlag = true;
  }
  else {
    Serial.println("🛑 STOP Command Received");
    stopNow = true;
    startSerpentineFlag = false;
    stopRover();
  }
}

// ==========================================================
// BASIC MOVEMENTS (STOP-SAFE)
// ==========================================================
void stopRover() {
  motor1.setSpeed(0);
  motor2.setSpeed(0);
}

void moveForwardMeters(float meters, float speedMps) {
  if (stopNow) return;

  int timeMs = (meters / speedMps) * 1000;

  motor1.setSpeed(130);
  motor2.setSpeed(130);

  unsigned long start = millis();
  while (millis() - start < timeMs) {
    if (stopNow) { stopRover(); return; }
  }

  stopRover();
}

void turnRight90() {
  if (stopNow) return;

  motor1.setSpeed(120);
  motor2.setSpeed(-120);

  unsigned long start = millis();
  while (millis() - start < turnTime90) {
    if (stopNow) { stopRover(); return; }
  }
  stopRover();
}

void turnLeft90() {
  if (stopNow) return;

  motor1.setSpeed(-120);
  motor2.setSpeed(120);

  unsigned long start = millis();
  while (millis() - start < turnTime90) {
    if (stopNow) { stopRover(); return; }
  }
  stopRover();
}

// ==========================================================
// SERPENTINE LOGIC
// ==========================================================
void serpentine(float L, float W, float S) {

  if (stopNow) return;

  int totalRows = max(1, (int)(W / S));
  bool goingForward = true;

  for (int lane = 0; lane < totalRows; lane++) {

    moveForwardMeters(L, forwardSpeedMps);
    if (stopNow) return;

    if (lane == totalRows - 1) break;

    if (goingForward) {
      turnRight90();
      moveForwardMeters(S, shiftSpeedMps);
      turnRight90();
    } else {
      turnLeft90();
      moveForwardMeters(S, shiftSpeedMps);
      turnLeft90();
    }

    if (stopNow) return;
    goingForward = !goingForward;
  }

  stopRover();
  Serial.println("✅ Serpentine COMPLETE");
}

// ==========================================================
// SETUP
// ==========================================================
void setup() {
  Serial.begin(115200);

  WiFi.mode(WIFI_STA);
  esp_wifi_set_channel(CHANNEL, WIFI_SECOND_CHAN_NONE);

  esp_now_init();
  esp_now_register_recv_cb(OnDataRecv);

  // Add master as peer
  esp_now_peer_info_t peerInfo = {};
  memcpy(peerInfo.peer_addr, masterMAC, 6);
  peerInfo.channel = CHANNEL;
  peerInfo.encrypt = false;
  esp_now_add_peer(&peerInfo);

  Serial.println("✅ Slave Ready");
}

// ==========================================================
// LOOP
// ==========================================================
void loop() {

  // ========== RECEIVE SENSOR DATA FROM ARDUINO ==========
  if (Serial.available()) {
    telemetryData.moisture = Serial.parseFloat();
    telemetryData.temperature = Serial.parseFloat();
    telemetryData.ec = Serial.parseFloat();
    telemetryData.ph = Serial.parseFloat();

    sendTelemetry();

    while (Serial.available()) Serial.read();
  }

  // ========== STOP HANDLER ==========
  if (stopNow) {
    stopRover();
    return;
  }

  // ========== START SERPENTINE ==========
  if (startSerpentineFlag) {
    startSerpentineFlag = false;

    serpentine(
      incomingData.fieldLength,
      incomingData.fieldWidth,
      incomingData.rowSpacing
    );
  }
}