SLAVE CODE FOR ROVER COMMUNICATION

CODE:

#include <esp_now.h>
#include <WiFi.h>
#include <esp_wifi.h>

#define CHANNEL 1

// ================= SLAVE MAC ADDRESS =================
// Replace with your SLAVE ESP32 MAC ID:
uint8_t slaveMAC[] = {0x1C, 0x69, 0x20, 0xC6, 0x73, 0xD8};

// ================= COMMAND STRUCT (MASTER → SLAVE) =================
typedef struct struct_message {
  float fieldLength;
  float fieldWidth;
  float rowSpacing;
  bool startAuto; // true = start serpentine, false = STOP
} struct_message;

struct_message outgoingData;

// ================= TELEMETRY STRUCT (SLAVE → MASTER) =================
typedef struct telemetry_message {
  float moisture;
  float temperature;
  float ec;
  float ph;
} telemetry_message;

telemetry_message incomingTelemetry;

// ==========================================================
// SEND STATUS CALLBACK
// ==========================================================
void OnDataSent(const uint8_t *mac_addr, esp_now_send_status_t status) {
  Serial.println(status == ESP_NOW_SEND_SUCCESS ? "✅ Sent" : "❌ Failed");
}

// ==========================================================
// RECEIVE SENSOR DATA CALLBACK
// ==========================================================
void OnDataRecv(const uint8_t * mac, const uint8_t *incomingData, int len) {
  if (len == sizeof(telemetry_message)) {
    memcpy(&incomingTelemetry, incomingData, sizeof(incomingTelemetry));

    Serial.println("\n📡 Telemetry Received:");
    Serial.print("Moisture: "); Serial.println(incomingTelemetry.moisture);
    Serial.print("Temperature: "); Serial.println(incomingTelemetry.temperature);
    Serial.print("EC: "); Serial.println(incomingTelemetry.ec);
    Serial.print("pH: "); Serial.println(incomingTelemetry.ph);
    Serial.println("----------------------------------");
  }
}

// ==========================================================
// SETUP
// ==========================================================
void setup() {
  Serial.begin(115200);

  WiFi.mode(WIFI_STA);
  esp_wifi_set_channel(CHANNEL, WIFI_SECOND_CHAN_NONE);

  if (esp_now_init() != ESP_OK) {
    Serial.println("❌ ERROR: ESP-NOW INIT FAILED");
    return;
  }

  esp_now_register_send_cb(OnDataSent);
  esp_now_register_recv_cb(OnDataRecv);

  // Add slave as peer
  esp_now_peer_info_t peerInfo = {};
  memcpy(peerInfo.peer_addr, slaveMAC, 6);
  peerInfo.channel = CHANNEL;
  peerInfo.encrypt = false;

  if (esp_now_add_peer(&peerInfo) != ESP_OK) {
    Serial.println("❌ Failed to add Slave");
    return;
  }

  Serial.println("✅ MASTER READY");
  Serial.println("Enter: Length Width RowSpacing OR press 'S' to STOP");
}

// ==========================================================
// LOOP
// ==========================================================
void loop() {

  if (Serial.available()) {

    // 👉 STOP COMMAND
    char c = Serial.peek();
    if (c == 'S' || c == 's') {

      while (Serial.available()) Serial.read(); // clear buffer

      outgoingData.fieldLength = 0;
      outgoingData.fieldWidth = 0;
      outgoingData.rowSpacing = 0;
      outgoingData.startAuto = false; // STOP FLAG

      esp_now_send(slaveMAC, (uint8_t*)&outgoingData, sizeof(outgoingData));

      Serial.println("\n🛑 STOP Command Sent!");
      Serial.println("----------------------------------");
      return;
    }

    // 👉 READ AUTOMATION INPUT
    float L = Serial.parseFloat();
    float W = Serial.parseFloat();
    float S = Serial.parseFloat();

    while (Serial.available()) Serial.read();

    if (L > 0 && W > 0 && S > 0) {

      outgoingData.fieldLength = L;
      outgoingData.fieldWidth = W;
      outgoingData.rowSpacing = S;
      outgoingData.startAuto = true;

      esp_now_send(slaveMAC, (uint8_t*)&outgoingData, sizeof(outgoingData));

      Serial.println("\n🚀 Automation Command Sent:");
      Serial.print("Length: "); Serial.println(L);
      Serial.print("Width: "); Serial.println(W);
      Serial.print("Spacing: "); Serial.println(S);
      Serial.println("----------------------------------");

    } else {
      Serial.println("❌ Invalid Input — Enter 3 positive numbers!");
    }

    delay(300);
  }
}
Master code